Heat Control

@ Hot Tub – 2 A; 1Di; 1Do

Water Temperature
Air Temperature
Controller Demand – 220V
Control:
Low-speed primary pump =
Demand AND
High Speed
hiTempBoiler = (InUse | heatTime) & TubDemand | (heatTime & poolDemand)
heatTub = (TubDemand & hiTempBoiler)
InUse = high-speed | UseDelay
Low-speed pump = (InUse | heatTub) & low-speed

@ Pool – 2A; 5Di; 7Do – 2 boards

Pool Temperature
Relative Humidity
Garage Demand
Storage Demand
Connector Demand
Modine Demand
Pool Floor Demand
Control:
Pool filter circulator
Pool heat circulator
Hot Tub circulator/zone valve
Garage circulator
Storage Circulator
Connector Circulator
Pool Floor Circulator

@ Bunker – 2A; 4Di; 1Do

Boiler Temp
DHW Temp
Floor Demand
Basement Demand
Stair Demand
DHW Demand
Control:
DHW Demand

MOSFET Solid State Switch 60VAC @ 500ma w/7.5ma in 21K5341 $2.34/ea
Opto Isolator 6 ma in; 5.5V logic; 75R5819; $2.54/ea